## Slide 1: Imperceptible Misclassification Attack on Deep Learning Accelerator by Glitch Injection
Wenye Liu1, Chip-Hong Chang1, Fan Zhang2 and Xiaoxuan Lou2
1School of Electrical and Electronic Engineering, Nanyang Technological University, Singapore
2College of Computer Science and Technology, Zhejiang University, China

## Slide 2: Speaker
Wenye Liu
I am currently pursuing a Ph.D. degree with the School of Electrical and Electronic Engineering, Nanyang Technological University, Singapore.
My research interests include machine learning accelerator, hardware security, and fault injection attack.
wliu015@e.ntu.edu.sg

## Slide 3: Edge Intelligence - AIoT
Deep learning algorithm on endpoint device
  Unlock edge applications
  Efficient hardware accelerator
Security and robustness considerations
  Existing vulnerabilities
  New potential attack vectors
Zhou et al. Proceedings of the IEEE 2019

## Slide 4: Existing Security flaws (1)
Input of adversarial examples
  Add carefully crafted perturbations on original sample
  Subvert correct prediction on well-trained classifier
Restrictions
  All the pixels should be shifted
  Any pixel can be altered to arbitrary value
Szegedy et al. ICLR 2014

## Slide 5: Existing Security flaws (2)
Model parameters interpolation
  Saturating last layer’s bias (ICCAD’17)
  Fault sneaking attack (DAC’19)
  Leave non-erasable traces in memory
Physical fault attack on edge DNN device
  Instruction skip faults by laser beam (CCS’18)
  Memory collision on dual-port RAM (FDTC’19)
  Evaluate on MCU or small-scale problem
Liu et al. ICCAD 2017
Alam et al. FDTC 2019
We introduce a stealthy misclassification attack on DNN accelerator for ImageNet applications

## Slide 6: General DNN Accelerator
Host processor and peripherals
Highly parallel and energy-efficient PE array
On-chip buffer and controller
PE array has a separate clock/voltage domain from other modules, which become an exploitable source of vulnerability

## Slide 7: Threat Model
Delude a physically deployed deep learning accelerator without leaving trace for detection
  Rule out invasive and tamper-evident probing attacks.
  No low-level implementation details
Black-box and gray-box penetrations
  No knowledge of DNN model
  Know model architecture and image

## Slide 8: Imperceptible Misclassification Attack
Disturb clock signal of the PE array
  Violate timing requirement in computation
  Corrupt intermediate results
  Leave no trace or faults in the circuit
Induce faults on DNN accelerator
  Multiplex clk_f_90 into clk_f by trigger
  leads to erroneous data
Timing Diagrams of Glitch Injection into Deep Learning Accelerator

## Slide 9: Black Box and Gray Box Attack
Black box setting
  Directly apply clk_mux to PE array
  Image and model independent attack
Gray box setting
  Induce faults on internal layer
  Minimize glitch injections
Evaluation platform on Xilinx ZCU102 board
Nine ImageNet models under evaluation

## Slide 10: Results of Black Box Attack
ImageNet - entire validation set
  50000 images
A set of glitch Intensity
  0.01% - 10%
> 98% misclassification on 8 models
  40% on VGG16
No clear distinctive relationship
Black-box Attack on Nine ImageNet Models
Vulnerability among Model Architectures

## Slide 11: Results of Gray Box Attack
Glitch injection on selected layer
  IMG44 is highly vulnerable
  IMG154 can only be misclassified on 5 layers
Effective Attack Pattern on ResNet50 of IMG44 and IMG154
Misclassify 256 images
  by glitch injection into one layer
  < 1.7% actual glitch intensity

## Slide 12: Potential Countermeasures
Improve the robustness of DNN models
  Defensive quantization (ICLR’19)
Employ one single domain of the accelerator
  Reduce energy efficiency
  Double DSP usage and 33.7% overhead of LUTs

## Slide 13: Conclusion
Inconspicuous attack on dedicated deep learning accelerator
  Perturb clock signal to the PE array infrequently
  Leave no sign after the attack
Demonstrate the attack on FPGA platform
  > 98% misclassification on 8 models in black box attack
  5.9x less glitch intensity to fool the classifier in gray box attack

## Slide 14: Questions